## Slide 1
Information Security Inc.
TRex

## Slide 2: Contents
About Trex
Current Challenges
Implications
Trex Stateful Features
Trex Stateless Features
Topology and the Testing Environment
Installing TRex
Using TRex
References

## Slide 3: About TRex
TRex is a traffic generator for Stateful and Stateless use cases
TRex -> realistic traffic generator

## Slide 4: Current Challenges
Cost : Commercial State-full traffic generators are expensive
Scale : Bandwidth does not scale up well with features complexity
Standardization : Lack of standardization of traffic patterns and methodologies
Flexibility : Commercial tools do not allow agility when flexibility and changes are needed

## Slide 5: Implications
High capital expenditure (capex) spent by different teams
Testing in low scale and extrapolation became a common practice, it is not accurate, and hides real life bottlenecks and quality issues
TRex addresses these problems through an innovative and extendable software implementation and by leveraging standard and open SW and x86/UCS HW.

## Slide 6: TRex Stateful Features
Fueled by DPDK
Generates and analyzes L4-7 traffic and able to provide in one tool capabilities provided by commercial L7 tools.
Stateful traffic generator based on pre-processing and smart replay of real traffic templates.
Generates and amplifies both client and server side traffic.
Customized functionality can be added.
Scale to 200Gb/sec for one UCS
Low cost

## Slide 7: TRex Stateless Features
Large scale - Supports about 10-30 million packets per second (mpps) per core, scalable with the number of cores
Profile can support multiple streams, scalable to 10K parallel streams
Interactive support - Fast Console, GUI
Statistics per interface
PCAP file import/export

## Slide 8: Topology
TRex testing topology -> TRex running in stateful mode
-> TRex emulates/creates a internal router
Router IP: 192.168.10.188
------------
| TRex |
| Client | IF1 IP: 192.168.10.105
| Side | ---------------
------------ | IF1 |
| DUT |
------------ | IF2 |
| TRex | ---------------
| Server | Cisco 2960
| Side | IF2 IP: 192.168.86.11
------------
Router IP: 192.168.86.188

## Slide 9: Topology

## Slide 10: Testing Environment
Ubuntu 14.04 LTS

## Slide 11: Installing TRex
Installing dependencies -> scapy

## Slide 12: Installing TRex
Installing dependencies -> g++

## Slide 13: Installing TRex
Installing dependencies -> zlib1g-dev

## Slide 14: Installing TRex
Cloning GitHub repository

## Slide 15: Installing TRex
Configuring TRex -> ./b configure

## Slide 16: Installing TRex
Building Trex -> ./b build

## Slide 17: Installing TRex
Building Trex -> ./b build

## Slide 18: Using TRex
Identify the ports

## Slide 19: Using TRex
TRex help menu

## Slide 20: Using TRex
Default config file -> /etc/trex_cfg.yaml

## Slide 21: Using TRex
Traffic config file -> in this example 255 clients talking to 240 servers

## Slide 22: Using TRex
Pcap file contents -> dns.pca, query for www.cisco.ip

## Slide 23: Using TRex
DUT config -> static routes

## Slide 24: Using TRex
Running TRex

## Slide 25: Using TRex
Tcpdump showing TRex DNS query (taken on another machine)

## Slide 26: References
TRex
https://trex-tgn.cisco.com/trex/
Ubuntu 14.04 LTS
http://old-releases.ubuntu.com/releases/14.04.1/ubuntu-14.04-desktop-amd64.iso
TRex Manual
https://trex-tgn.cisco.com/trex/doc/trex_manual.html